## Slide 1: Memory-based FFT
SEUNGWAN NOH

## Slide 2: Contents
Fast Fourier Transform
Block RAM/ROM
FFT Implementations
  SPBRAM
  Simple DPBRAM
  True DPBRAM

## Slide 3: FFT
DFT(Discrete Fourier Transform)
Computation of DFT
  N=4
    16 Complex Multiplication
    12 Complex Addition
Notes: FFT 알고리즘 내용 보충

## Slide 4: FFT
Computation of DFT
N | # of Multiplication | # of Addition
4 | 16 | 12
8 | 64 | 56
16 | 256 | 240
64 | 1024 | 992
N | N2 | N(N-1)

## Slide 5: FFT
FFT(Fast Fourier Transform)
  FFT is an algorithm used to efficiently compute DFT.
  FFT reduces the number of operations to compute DFT.
Cooley-Tuckey Algorithm
  James Cooley and John Tuckey in 1965
  Reducing the computational complexity from N2 to NlogN
  “Divide and Conquer”
  Periodicity and symmetry of DFT

## Slide 6: Cooley-Tuckey Algorithm
DIT(Decimation in Time)
  Partitioning the sequence in time.
  Divide the original sequence into even and odd-indexed.
  DIT algorithm essentially reorders the sequence in bit-reversed manner as part of its process.
DIF(Decimation in Frequency)
  Partitioning the sequence in frequency.
  Computing the DFT outputs and decimating them into even and odd components.
  Involves rearrangement of the output sequence.
Radix-2 Algorithm
  Applicable when the length of the sequence is power of two.
  Divide DFT computation into two parts at each stage.

## Slide 7: Cooley-Tuckey Algorithm
Derivation of the DIT Radix-2 FFT Algorithm
  DFT
  Break into two parts

## Slide 8: Cooley-Tuckey Algorithm
Derivation of the DIT Radix-2 FFT Algorithms
  Upper half of the DFT outputs

## Slide 9: Cooley-Tuckey Algorithm
Derivation of the DIT Radix-2 FFT Algorithms
  Simplify the equations

## Slide 10: Cooley-Tuckey Algorithm
Radix-2 8pt DIT FFT SFG

## Slide 11: Cooley-Tuckey Algorithm
DIF
  Natural order input >> Bit-reversal output
DIT
  Bit-reversal input >> Natural order output

## Slide 12: Block RAM/ROM
Single-port
  Has one access port, read or write data in one cycle.
  Sequential access, low throughput
  Enhance efficiency, reduce area, and minimize power.
Dual-port Memory
  Has two access ports, simultaneous read and write.
  High throughput
  More complex and expensive.
  Require more complex access control

## Slide 13: Memory-based FFT
MBFFT |  |  |  |  | 
BRAM |  | SPBRAM |  | Simple DPBRAM | True DPBRAM
Point | 16pt |  | 64pt | 16pt | 16pt
LUT | 184 |  | 234 | 255 | 291
FF | 119 |  | 126 | 222 | 56
BRAM | 2 |  | 2 | 2.50 | 3.50
DSP | 4 |  | 4 | 4 | 4
IO | 69 |  | 69 | 69 | 133
BUFG | 1 |  | 1 | 1 | 1
WNS(ns) | 6.566 |  | 7.055 | 7.101 | 8.136
WHS(ns) | 0.217 |  | 0.131 | 1.63 | 0.177
Power(W) | 0.119 |  | 0.12 | 0.122 | 0.13

## Slide 14: SPBRAM FFT

## Slide 15: SPBRAM
SPBRAM
  Block Diagram
  Timing Diagram
  Radix-2 16pt DIT MBFFT
  Simulation Results
  Reusable Design

## Slide 16: Block Diagram

## Slide 17: Timing Diagram

## Slide 18: Radix-2 16pt DIT MBFFT
FSM
  PRE_IN, IDLE, RUN, STAGE_N
Counter
  cnt, cnt_in, cnt_out, cnt_dly, cnt_CROM
Enable CLs
  we_AMEM, we_BMEM, we_OMEM
MUX select
  sel_input, sel_res, sel_mem
Handshake
  in_rdy, out_vld
Address
  AMEM, BMEM, OMEM, CROM

## Slide 19: Radix-2 16pt DIT MBFFT
N = 4, = 16pt
N Stages for each Set
  Set 1 has Pre-stage for data input
N+1 bits counter for memory address
N/2 bits for State parameters
2**N + 2 cycles per stage
  Pipeline depth is 3 (3 registers in FFT)
    2**4 = 16, 16 + 2 = 18
    [0:18]; 19 cycles

## Slide 20: Radix-2 16pt DIT MBFFT
FSM
cstate are 1 cycle delay by nstate
cstate_in
  PRE_IN >> RUN
    in_vld == 1, after nrst
  RUN >> IDLE
    LCNT – 3, after finish external data input
    LCNT = 2**N + 2 // 18 cycles
  IDLE >> RUN
    In STAGE_4, after 3 cycles
    external data input for next set of FFT

## Slide 21: Radix-2 16pt DIT MBFFT
cstate
IDLE >> STAGE_1
  nstate_in == IDLE, after finish ext_data_in
STAGE T >> STAGE T+1
  After LCNT move to next stage
  STAGE_4 >> STAGE_1

## Slide 22: Radix-2 16pt DIT MBFFT
cstate_out
IDLE >> RUN
  After current set finished
RUN >> IDLE
  After outputting all FFT result

## Slide 23: Radix-2 16pt DIT MBFFT
Counters
cnt
  Count until LCNT
cnt_in
  Count when ext_data_in is inputting
cnt_out
  Count when outputting the FFT result

## Slide 24: Radix-2 16pt DIT MBFFT
Control signals
  Register Enable
    en_REG_A is high; (0 index digit of binary counter) == 1
    en_REG_B is 1 cycle delay to A, C is 1 cycle delay to B
  Memory Write Enable
    ~we_AMEM; Pre-stage and Even # stages after 3 cycles
    ~we_BMEM; Odd # stages after 3 cycles
    ~we_OMEM; cstate_in == RUN and Stage 4
    Pipeline depth for each stage is 3 cycles

## Slide 25: Radix-2 16pt DIT MBFFT
Control signals
  Input ready and Output valid signals
    out_vld; cstate_out == RUN and cnt_out == TRUE
    1 cycle delay because of data_rd_OMEM
  MUX control signals
    sel_input; 0 >> out_FFT, 1 >> ext_data_in
    sel_res; 0 >> out_REG_C, 1 >> out1_BF
    sel_mem; 0 >> AMEM, 1 >> BMEM

## Slide 26: Radix-2 64pt DIT MBFFT
Control signals for, N = 6

## Slide 27: Radix-2 16pt DIT MBFFT
Bit-reversed ext_data_in for DIT FFT
= 16pt FFT has N = 4 stages
Address distance of each BF for Stage T is
  Stage1 (0,1), (2,3), (4,5), (6,7), (8,9), (10,11), (12,13), (14,15)
  Stage2 (0,2), (1,3), (4,6), (5,7), (8,10), (9,11), (12,14), (13,15)
  Stage3 (0,4), (1,5), (2,6), (3,7), (8,12), (9,13), (10,14), (11,15)
  Stage4 (0,8), (1,9), (2,10), (3,11), (4,12), (5,13), (6,14), (7,15)
    ext_data_in for the next FFT set
Set T+1
  Stage1

## Slide 28: Radix-2 16pt DIT MBFFT
RD address and WR address is same in each stage
  In-place
  If RD in AMEM (0,2), then WR in BMEM (0,2)
AMEM, BMEM Address
  Pre-stage (ext_data_in  Write AMEM)
  Stage1 (Read AMEM  Write BMEM)
  Stage2 (Read BMEM  Read AMEM)
  Stage3 (Read AMEM  Write BMEM)
  Stage4 (Read BMEM  Write OMEM)
Same for 64pt, the only change is N = 6

## Slide 29: Radix-2 16pt DIT MBFFT
OMEM Address
  Same as BMEM address in Stage4; (k,k+8), k = 0 ~ 7
  Same as cnt_out in the next set Stage1
  Bit-reversal input >> Natural order output
ROM Address
  Stage1; 0
  Stage2; {0, cnt[0], 0, 0}//4*cnt[0]
  Stage3; {0, cnt[1], cnt[0], 0}//4*cnt[1]+2*cnt[0]
  Stage4; Same as cnt value

## Slide 30: Radix-2 16pt DIT MBFFT
Addresses for 16pt FFT

## Slide 31: Radix-2 64pt DIT MBFFT
FFT 64pt shares the same architecture with 16pt but,
  Address bit-width has increased; N = 4 >> N = 6
  Two more stages; 6 – 4 = 2
  2**N + 2 cycles per stage; 66 cycles
  All modules are reusable, but controller

## Slide 32: Radix-2 64pt DIT MBFFT
Two more stage parameters
  Stage 5 and 6
LCNT is now 66
  Pipeline depth = 3
Address distance of each BF for Stage T is
  Stage5 (0,16), (1,17), (2,18), … , (46, 62), (47,63)
  Stage6 (0,32), (1,33), (2,34), … , (15,47), (31,63)

## Slide 33: Radix-2 64pt DIT MBFFT
Addresses for 64pt FFT

## Slide 34: Radix-2 16pt DIT MBFFT
AMEM(32x16) |  |  |  |  |  | 
cstate | IDLE | STAGE_1 | STAGE_2 | STAGE_3 | STAGE_4 | STAGE_1
addr | data_wr | data_rd | data_wr | data_rd | data_wr | data_rd
0000 | x[0] | x[0] | b[0] | b[0] | x2[0] | x2[0]
0001 | x[8] | x[8] | b[1] | b[1] | x2[8] | x2[8]
0010 | x[4] | x[4] | b[2] | b[2] | x2[4] | x2[4]
0011 | x[12] | x[12] | b[3] | b[3] | x2[12] | x2[12]
0100 | x[2] | x[2] | b[4] | b[4] | x2[2] | x2[2]
0101 | x[10] | x[10] | b[5] | b[5] | x2[10] | x2[10]
0110 | x[6] | x[6] | b[6] | b[6] | x2[6] | x2[6]
0111 | x[14] | x[14] | b[7] | b[7] | x2[14] | x2[14]
1000 | x[1] | x[1] | b[8] | b[8] | x2[1] | x2[1]
1001 | x[9] | x[9] | b[9] | b[9] | x2[9] | x2[9]
1010 | x[5] | x[5] | b[10] | b[10] | x2[5] | x2[5]
1011 | x[13] | x[13] | b[11] | b[11] | x2[13] | x2[13]
1100 | x[3] | x[3] | b[12] | b[12] | x2[3] | x2[3]
1101 | x[11] | x[11] | b[13] | b[13] | x2[11] | x2[11]
1110 | x[7] | x[7] | b[14] | b[14] | x2[7] | x2[7]
1111 | x[15] | x[15] | b[15] | b[15] | x2[15] | x2[15]

## Slide 35: Radix-2 16pt DIT MBFFT
BMEM(32x16) |  |  |  |  |  | 
cstate | IDLE | STAGE_1 | STAGE_2 | STAGE_3 | STAGE_4 | STAGE_1
addr | data_wr | data_rd | data_wr | data_rd | data_wr | data_rd
0000 |  | a[0] | a[0] | c[0] | c[0] | a2[0]
0001 |  | a[1] | a[1] | c[1] | c[1] | a2[1]
0010 |  | a[2] | a[2] | c[2] | c[2] | a2[2]
0011 |  | a[3] | a[3] | c[3] | c[3] | a2[3]
0100 |  | a[4] | a[4] | c[4] | c[4] | a2[4]
0101 |  | a[5] | a[5] | c[5] | c[5] | a2[5]
0110 |  | a[6] | a[6] | c[6] | c[6] | a2[6]
0111 |  | a[7] | a[7] | c[7] | c[7] | a2[7]
1000 |  | a[8] | a[8] | c[8] | c[8] | a2[8]
1001 |  | a[9] | a[9] | c[9] | c[9] | a2[9]
1010 |  | a[10] | a[10] | c[10] | c[10] | a2[10]
1011 |  | a[11] | a[11] | c[11] | c[11] | a2[11]
1100 |  | a[12] | a[12] | c[12] | c[12] | a2[12]
1101 |  | a[13] | a[13] | c[13] | c[13] | a2[13]
1110 |  | a[14] | a[14] | c[14] | c[14] | a2[14]
1111 |  | a[15] | a[15] | c[15] | c[15] | a2[15]

## Slide 36: Radix-2 16pt DIT MBFFT
OMEM(32X16) |  | 
cstate | STAGE_4 | STAGE_1
addr | data_wr | data_rd
0000 | y[0] | y[0]
0001 | y[1] | y[1]
0010 | y[2] | y[2]
0011 | y[3] | y[3]
0100 | y[4] | y[4]
0101 | y[5] | y[5]
0110 | y[6] | y[6]
0111 | y[7] | y[7]
1000 | y[8] | y[8]
1001 | y[9] | y[9]
1010 | y[10] | y[10]
1011 | y[11] | y[11]
1100 | y[12] | y[12]
1101 | y[13] | y[13]
1110 | y[14] | y[14]
1111 | y[15] | y[15]
CROM(32x8) | 
addr | data
0000 | 00007FFE
0001 | CF047642
0010 | A57E5A82
0011 | 89BE30FC
0100 | 80020000
0101 | 89BECF04
0110 | A57EA57E
0111 | CF0489BE

## Slide 37: STAGE_1

## Slide 38: STAGE_2

## Slide 39: STAGE_3

## Slide 40: STAGE_4

## Slide 41: SET 2

## Slide 42: Simulation Results
SPBRAM 16pt
  Behavioral simulation
  Post-Synthesis Timing simulation
  Post-Implementation Timing simulation

## Slide 43: Simulation Results
SPBRAM 16pt

## Slide 44: Simulation Results
SPBRAM 64pt
  Behavioral simulation
  Post-Synthesis Timing simulation
  Post-Implementation Timing simulation

## Slide 45: Simulation Results
SPBRAM 64pt

## Slide 46: Reusable Design
Operation Cycles
  External data write into AMEM
  Cycle 0: Read assert to AMEM in bit-reversed order
  Cycle 1: Mem data >> REG_A
  Cycle 2: MEM data >> MULT >> REG_B
  Cycle 3: REG_A, REG_B >> REG_C, out_BF1
  Cycle 4: REG_C >> BMEM
  Cycle 5: out_BF1 >> BMEM

## Slide 47: Reusable Design
Stage, Butterfly Unit, Index (n,b,k)
  n = [0, log2(N) - 1]
  b = [0, N/2**n - 1]
  k = [0, 2**n - 1]
  N = 16 points
    x[0] >> (0,0,0)
    x[6] >> (0,3,0)
    a[2] >> (0,0,1)
    b[7] >> (2,0,7)

## Slide 48: Reusable Design
addr
  (1 << cnt_n)*cnt_b + cnt_k + cnt_i*(1 << (cnt_n - 1))
addr_CROM
  (1 << (N-cnt_n))*cnt_k

## Slide 49: Reusable Design
Bit-reversed input
  cnt (0~15)

## Slide 50: Reusable Design
Stage 1
  n = 0
  b = 0 ~ 7
  k = 0

## Slide 51: Reusable Design
Stage 2
  n = 1
  b = 0 ~ 3
  k = 0 ~ 1

## Slide 52: Reusable Design
Stage 3
  n = 2
  b = 0 ~ 1
  k = 0 ~ 3

## Slide 53: Reusable Design
Stage 4
  n = 3
  b = 0
  k = 0 ~ 7

## Slide 54: Reusable Design
controller.v
module controller #(
PNT = 16,
N = $clog2(PNT) // STAGE
)(
input clk,
input rstn,
input in_vld,
input out_rdy,
output wire in_rdy,
output wire out_vld,
output wire sel_input,
output wire sel_res,
output wire sel_mem,
output wire we_AMEM,
output wire we_BMEM,
output wire we_OMEM,
output wire [N-1:0] addr_AMEM,
output wire [N-1:0] addr_BMEM,
output wire [N-1:0] addr_OMEM,
output wire [9:0] addr_CROM,
output wire en_REG_A,
output reg en_REG_B,
output reg en_REG_C
);
wire [$clog2(N):0] last_n;
wire [$clog2(PNT/2):0] last_b;
wire [$clog2(PNT/2):0] last_k;
assign last_n = N;
assign last_b = PNT/(1 << cnt_n) - 1;
assign last_k = (1 << (cnt_n-1)) - 1;
assign last_i = 1;
// Counter
reg [N:0] cnt;
always @(posedge clk or negedge rstn) begin
if (!rstn) begin
cnt <= 0;
end else begin
if (state == IDLE) begin
cnt <= (cnt == PNT-1) ? 0 : cnt+1;
end else if (state == RUN || state == BUBL) begin
cnt <= (cnt == PNT-1 + 3) ? 0 : cnt+1; // Pipeline depth: 3
end else cnt <= cnt;
end
end

## Slide 55: Reusable Design
controller.v
reg [$clog2(8192):0] cnt_s;
reg [$clog2(8192):0] tmp_cnt_s;
reg [$clog2(N):0] cnt_n;
reg [$clog2(N):0] tmp_cnt_n;
reg [$clog2(PNT/2):0] cnt_b;
reg [$clog2(PNT/2):0] cnt_k;
reg cnt_i;
always @(posedge clk or negedge rstn) begin
if (!rstn) begin
cnt_s <= 0; // SET
tmp_cnt_s <= 0;
end
else begin
if (cnt_n == last_n && cnt_b == last_b && cnt_k == last_k && cnt_i == last_i)
tmp_cnt_s = cnt_s + 1;
else if (cnt == PNT+2 && state == BUBL)
cnt_s <= tmp_cnt_s;
end
end

## Slide 56: Reusable Design
controller.v
always @(posedge clk or negedge rstn) begin
if (!rstn) begin
cnt_n <= 0; // STAGE
tmp_cnt_n <= 0;
cnt_b <= 0; // BU
cnt_k <= 0; // INDEX
cnt_i <= 0; // 0,1
end else if (state == RUN) begin
if (cnt_b == last_b && cnt_k == last_k && cnt_i == last_i) begin
tmp_cnt_n <= (cnt_n == last_n) ? 1 : cnt_n+1;
cnt_b <= 0;
cnt_k <= 0;
cnt_i <= 0;
end else if (cnt_k == last_k && cnt_i == last_i) begin
cnt_b <= (cnt_b == last_b) ? 0 : cnt_b+1;
cnt_k <= 0;
cnt_i <= 0;
end else if (cnt_i == last_i) begin
cnt_k <= (cnt_k == last_k) ? 0 : cnt_k+1;
cnt_i <= 0;
end else cnt_i <= (cnt_i == last_i) ? 0 : cnt_i+1;
end else if (state == IDLE) begin
if (cnt == PNT-1) cnt_n <= cnt_n + 1;
end else if (cnt == PNT+2 && state == BUBL) begin
cnt_n <= tmp_cnt_n;
cnt_b <= 0;
cnt_k <= 0;
cnt_i <= 0;
end else begin
cnt_n <= cnt_n;
cnt_b <= cnt_b;
cnt_k <= cnt_k;
cnt_i <= cnt_i;
end
end

## Slide 57: Reusable Design
controller.v
// FSM
localparam BUBL = 2'b00;
localparam IDLE = 2'b10;
localparam RUN = 2'b11;
reg [1:0] state;
reg [1:0] next;
always @(posedge clk or negedge rstn) begin
if (!rstn) begin
state <= IDLE;
end else begin
state <= next;
end
end
always @(*) begin
case(state)
IDLE: begin
if (cnt == PNT-1) next <= RUN;
else next <= IDLE;
end
RUN : begin
if (cnt_b == last_b && cnt_k == last_k && cnt_i == last_i)
next <= BUBL;
else next <= RUN;
end
BUBL: begin
if (cnt_n == 0 && cnt == PNT+2) next <= RUN;
if (cnt == PNT+2) next <= RUN;
else next <= BUBL;
end
default: next <= IDLE;
endcase
end

## Slide 58: Reusable Design
controller.v
assign en_REG_A = (state == RUN) ? cnt[0] : 0;
always @(posedge clk or negedge rstn) begin
if (!rstn) begin
en_REG_B <= 0;
en_REG_C <= 0;
end else if (state == RUN || state == BUBL) begin
en_REG_B <= en_REG_A;
en_REG_C <= en_REG_B;
end else begin
en_REG_B <= en_REG_B;
en_REG_C <= en_REG_C;
end
end
reg [1:0] mode_reg;
wire [1:0] mode;
always @(posedge clk or negedge rstn) begin
if (!rstn) mode_reg <= 0;
else if (state == RUN) mode_reg <= mode;
else mode_reg <= mode_reg;
end
assign mode = (state == IDLE) ? 2'b11
: (state == RUN && cnt_n % 2 == 1) ? 2'b10 // RD(A), WR(B)
: (state == RUN && cnt_n % 2 == 0) ? 2'b01 // RD(B), WR(A)
: (state == BUBL) ? mode_reg : 0;
assign we_AMEM = (mode == 2'b11 || (cnt>2 && mode == 2'b01)) ? 1'b1 : 1'b0;
assign we_BMEM = ((cnt>2) && mode == 2'b10) ? 1'b1 : 1'b0;
assign we_OMEM = (cnt>2 && mode == 2'b01) ? 1'b1 : 1'b0;
assign sel_input = in_rdy;
assign sel_mem = (mode == 2'b10) ? 1'b0 // RD AMEM
: (mode == 2'b01) ? 1'b1 // RD BMEM
: 'b0;
assign sel_res = en_REG_C;

## Slide 59: Reusable Design
controller.v
wire [N:0] cntd;
assign cntd = (cnt>0) ? cnt-1 : 'b0; // 1 cycle delayed counter
assign in_rdy = (cnt_n == 0 || (cnt>2 && cnt_n == last_n)) ? 1'b1 : 1'b0;
assign out_vld = (!cnt_s) ? 1'b0 : (cnt>0 && cnt_n == 1 && cntd<PNT) ? 1'b1 : 1'b0; // set 2 부터
// DIT input
function [N-1:0] bit_reverse;
input [N-1:0] in;
integer i;
begin
for (i=0; i<N; i=i+1) begin
bit_reverse[i] = in[N-1-i];
end
end
endfunction
reg [N-1:0] tmp1_addr_d, tmp2_addr_d, addr_d; // delayed by pipeline depth: 3
wire [N-1:0] addr;
wire [N-1:0] cnt_scaled = cnt[N-1:0];
assign addr = (state == IDLE) ? bit_reverse(cnt_scaled)
: (1 << cnt_n)*cnt_b + cnt_k + cnt_i*(1 << (cnt_n-1));
always @(posedge clk or negedge rstn) begin
if (!rstn) begin
tmp1_addr_d <= 0;
tmp2_addr_d <= 0;
addr_d <= 0;
end else begin
tmp1_addr_d <= addr;
tmp2_addr_d <= tmp1_addr_d;
addr_d <= tmp2_addr_d;
end
end

## Slide 60: Reusable Design
controller.v
wire [N-1:0] cnt_scaled_d;
assign cnt_scaled_d = (cnt>2) ? cnt-3 : 'b0;
assign addr_AMEM = (cnt_n == last_n) ? bit_reverse(cnt_scaled_d) // Next set input
: (mode == 2'b10 || mode == 2'b11) ? addr // First set input or RD(A), WR(B)
: (mode == 2'b01) ? addr_d // RD(B), WR(A)
: 'b0;
assign addr_BMEM = (mode == 2'b01) ? addr
: (mode == 2'b10) ? addr_d
: 'b0;
assign addr_OMEM = (cnt_n == last_n) ? addr_d
:((mode == 2'b10 && cnt_n == 1) && cnt<PNT) ? cnt
: 'b0;
reg [9:0] tmp1_addr_CROM;
wire [9:0] tmp0_addr_CROM;
assign tmp0_addr_CROM = (1 << (N-cnt_n))*cnt_k;
always @(posedge clk or negedge rstn) begin
if (!rstn) begin
tmp1_addr_CROM <= 0;
//tmp2_addr_CROM <= 0;
end else begin
tmp1_addr_CROM <= tmp0_addr_CROM;
//tmp2_addr_CROM <= tmp1_addr_CROM;
end
end
assign addr_CROM = tmp1_addr_CROM;
endmodule

## Slide 61: Reusable Design

## Slide 62: Simple DPBRAM

## Slide 63
Simple DPBRAM
  Vertex Coloring
    DIF
    DIT
  Block Diagram
  Timing Diagram
  Verilog Implementation
  Simulation Results

## Slide 64: Vertex Coloring
DIT FFT
  Bit-reversed Input
bank0
[1] Hsin-Fu Lo, Ming-Der Shieh and Chien-Ming Wu, "Design of an efficient FFT processor for DAB system," ISCAS 2001. The 2001 IEEE International Symposium on Circuits and Systems (Cat. No.01CH37196), Sydney, NSW, Australia, 2001, pp. 654-657 vol. 4, doi: 10.1109/ISCAS.2001.922322.

## Slide 65: Vertex Coloring
Address for DIF 16pt
  Natural order inputs >> Bit-reversed outputs
  Stage 1: (0,4), (4,0), (5,1), (1,5), (6,2), (2,6), (3,7), (7,3)
  Stage 2: (0,2), (2,0), (3,1), (1,3), (6,4), (4,6), (5,7), (7,7)
  Stage 3: (0,1), (1,0), (3,2), (2,3), (5,4), (4,5), (6,7), (7,6)
  Stage 4: (0,0), (1,1), (2,2), (3,3), (4,4), (5,5), (6,6), (7,7)
Address for DIT 16pt
  Bit-reversed inputs >> Natural order outputs
  Stage 1: (0,0), (1,1), (2,2), (3,3), (4,4), (5,5), (6,6), (7,7)
  Stage 2: (0,1), (1,0), (3,2), (2,3), (5,4), (4,5), (6,7), (7,6)
  Stage 3: (0,2), (2,0), (3,1), (1,3), (6,4), (4,6), (5,7), (7,7)
  Stage 4: (0,4), (4,0), (5,1), (1,5), (6,2), (2,6), (3,7), (7,3)

## Slide 66
Simple DPBRAM
  Vertex Coloring
    DIF
    DIT
  Block Diagram
  Timing Diagram
  Verilog Implementation
  Simulation Results

## Slide 67: Vertex Coloring
addr | BANK0 | BANK1
000 | x[0] | x[1]
001 | x[3] | x[2]
010 | x[5] | x[4]
011 | x[6] | x[7]
100 | x[9] | x[8]
101 | x[10] | x[11]
110 | x[12] | x[13]
111 | x[15] | x[14]
addr | BANK0 | BANK1
000 | a[0] | x[1]
001 | x[3] | x[2]
010 | x[5] | x[4]
011 | x[6] | x[7]
100 | x[9] | a[8]
101 | x[10] | x[11]
110 | x[12] | x[13]
111 | x[15] | x[14]
addr | BANK0 | BANK1
000 | a[0] | a[1]
001 | x[3] | x[2]
010 | x[5] | x[4]
011 | x[6] | x[7]
100 | a[9] | a[8]
101 | x[10] | x[11]
110 | x[12] | x[13]
111 | x[15] | x[14]
addr | BANK0 | BANK1
000 | a[0] | a[1]
001 | x[3] | a[2]
010 | x[5] | x[4]
011 | x[6] | x[7]
100 | a[9] | a[8]
101 | a[10] | x[11]
110 | x[12] | x[13]
111 | x[15] | x[14]

## Slide 68: Vertex Coloring
addr | BANK0 | BANK1
000 | a[0] | a[1]
001 | a[3] | a[2]
010 | x[5] | x[4]
011 | x[6] | x[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | x[12] | x[13]
111 | x[15] | x[14]
addr | BANK0 | BANK1
000 | a[0] | a[1]
001 | a[3] | a[2]
010 | x[5] | a[4]
011 | x[6] | x[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | a[12] | x[13]
111 | x[15] | x[14]
addr | BANK0 | BANK1
000 | a[0] | a[1]
001 | a[3] | a[2]
010 | a[5] | a[4]
011 | x[6] | x[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | a[12] | a[13]
111 | x[15] | x[14]
addr | BANK0 | BANK1
000 | a[0] | a[1]
001 | a[3] | a[2]
010 | a[5] | a[4]
011 | a[6] | x[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | a[12] | a[13]
111 | x[15] | a[14]

## Slide 69: Vertex Coloring
addr | BANK0 | BANK1
000 | a[0] | a[1]
001 | a[3] | a[2]
010 | a[5] | a[4]
011 | a[6] | a[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | a[12] | a[13]
111 | a[15] | a[14]
addr | BANK0 | BANK1
000 | b[0] | a[1]
001 | a[3] | a[2]
010 | a[5] | b[4]
011 | a[6] | a[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | a[12] | a[13]
111 | a[15] | a[14]
addr | BANK0 | BANK1
000 | b[0] | b[1]
001 | a[3] | a[2]
010 | b[5] | b[4]
011 | a[6] | a[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | a[12] | a[13]
111 | a[15] | a[14]
addr | BANK0 | BANK1
000 | b[0] | b[1]
001 | a[3] | b[2]
010 | b[5] | b[4]
011 | b[6] | a[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | a[12] | a[13]
111 | a[15] | a[14]

## Slide 70: Vertex Coloring
addr | BANK0 | BANK1
000 | b[0] | b[1]
001 | b[3] | b[2]
010 | b[5] | b[4]
011 | b[6] | b[7]
100 | a[9] | a[8]
101 | a[10] | a[11]
110 | a[12] | a[13]
111 | a[15] | a[14]
addr | BANK0 | BANK1
000 | b[0] | b[1]
001 | b[3] | b[2]
010 | b[5] | b[4]
011 | b[6] | b[7]
100 | a[9] | b[8]
101 | a[10] | a[11]
110 | b[12] | a[13]
111 | a[15] | a[14]
addr | BANK0 | BANK1
000 | b[0] | b[1]
001 | b[3] | b[2]
010 | b[5] | b[4]
011 | b[6] | b[7]
100 | b[9] | b[8]
101 | a[10] | a[11]
110 | b[12] | b[13]
111 | a[15] | a[14]
addr | BANK0 | BANK1
000 | b[0] | b[1]
001 | b[3] | b[2]
010 | b[5] | b[4]
011 | b[6] | b[7]
100 | b[9] | b[8]
101 | b[10] | a[11]
110 | b[12] | b[13]
111 | a[15] | b[14]

## Slide 71: Vertex Coloring
addr | BANK0 | BANK1
000 | b[0] | b[1]
001 | b[3] | b[2]
010 | b[5] | b[4]
011 | b[6] | b[7]
100 | b[9] | b[8]
101 | b[10] | b[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | b[1]
001 | b[3] | c[2]
010 | b[5] | b[4]
011 | b[6] | b[7]
100 | b[9] | b[8]
101 | b[10] | b[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | b[5] | b[4]
011 | b[6] | b[7]
100 | b[9] | b[8]
101 | b[10] | b[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | b[9] | b[8]
101 | b[10] | b[11]
110 | b[12] | b[13]
111 | b[15] | b[14]

## Slide 72: Vertex Coloring
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | b[9] | b[8]
101 | b[10] | b[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | b[9] | c[8]
101 | c[10] | b[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | c[12] | b[13]
111 | b[15] | c[14]

## Slide 73: Vertex Coloring
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | b[9] | b[8]
101 | b[10] | b[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | b[9] | c[8]
101 | c[10] | b[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | b[12] | b[13]
111 | b[15] | b[14]
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | c[12] | b[13]
111 | b[15] | c[14]

## Slide 74: Vertex Coloring
addr | BANK0 | BANK1
000 | c[0] | c[1]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | c[12] | c[13]
111 | c[15] | c[14]
addr | BANK0 | BANK1
000 | y[0] | y[8]
001 | c[3] | c[2]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | c[12] | c[13]
111 | c[15] | c[14]
addr | BANK0 | BANK1
000 | y[0] | y[8]
001 | y[12] | y[4]
010 | c[5] | c[4]
011 | c[6] | c[7]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | c[12] | c[13]
111 | c[15] | c[14]
addr | BANK0 | BANK1
000 | y[0] | y[8]
001 | y[12] | y[4]
010 | y[10] | y[2]
011 | c[6] | c[7]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | c[12] | c[13]
111 | c[15] | c[14]

## Slide 75: Vertex Coloring
addr | BANK0 | BANK1
000 | y[0] | y[8]
001 | y[12] | y[4]
010 | y[10] | y[2]
011 | y[6] | y[14]
100 | c[9] | c[8]
101 | c[10] | c[11]
110 | c[12] | c[13]
111 | c[15] | c[14]
addr | BANK0 | BANK1
000 | y[0] | y[8]
001 | y[12] | y[4]
010 | y[10] | y[2]
011 | y[6] | y[14]
100 | y[9] | y[1]
101 | c[10] | c[11]
110 | c[12] | c[13]
111 | c[15] | c[14]
addr | BANK0 | BANK1
000 | y[0] | y[8]
001 | y[12] | y[4]
010 | y[10] | y[2]
011 | y[6] | y[14]
100 | y[9] | y[1]
101 | y[5] | y[14]
110 | c[12] | c[13]
111 | c[15] | c[14]
addr | BANK0 | BANK1
000 | y[0] | y[8]
001 | y[12] | y[4]
010 | y[10] | y[2]
011 | y[6] | y[14]
100 | y[9] | y[1]
101 | y[5] | y[13]
110 | y[3] | y[11]
111 | c[15] | c[14]

## Slide 76
Simple DPBRAM
  Vertex Coloring
    DIF
    DIT
  Block Diagram
  Timing Diagram
  Verilog Implementation
  Simulation Results

## Slide 77: Vertex Coloring
addr | BANK0 | BANK1
000 | x[0] | x[8]
001 | x[12] | x[4]
010 | x[10] | x[2]
011 | x[6] | x[14]
100 | x[9] | x[1]
101 | x[5] | x[13]
110 | x[3] | x[11]
111 | x[15] | x[7]
addr | BANK0 | BANK1
000 | A[0] | A[1]
001 | x[12] | x[4]
010 | x[10] | x[2]
011 | x[6] | x[14]
100 | x[9] | x[1]
101 | x[5] | x[13]
110 | x[3] | x[11]
111 | x[15] | x[7]
addr | BANK0 | BANK1
000 | A[0] | A[1]
001 | A[3] | A[2]
010 | x[10] | x[2]
011 | x[6] | x[14]
100 | x[9] | x[1]
101 | x[5] | x[13]
110 | x[3] | x[11]
111 | x[15] | x[7]
addr | BANK0 | BANK1
000 | A[0] | A[1]
001 | A[3] | A[2]
010 | A[5] | A[4]
011 | x[6] | x[14]
100 | x[9] | x[1]
101 | x[5] | x[13]
110 | x[3] | x[11]
111 | x[15] | x[7]

## Slide 78: Vertex Coloring
addr | BANK0 | BANK1
000 | A[0] | A[1]
001 | A[3] | A[2]
010 | A[5] | A[4]
011 | A[6] | A[7]
100 | x[9] | x[1]
101 | x[5] | x[13]
110 | x[3] | x[11]
111 | x[15] | x[7]
addr | BANK0 | BANK1
000 | A[0] | A[1]
001 | A[3] | A[2]
010 | A[5] | A[4]
011 | A[6] | A[7]
100 | A[9] | A[8]
101 | x[5] | x[13]
110 | x[3] | x[11]
111 | x[15] | x[7]
addr | BANK0 | BANK1
000 | A[0] | A[1]
001 | A[3] | A[2]
010 | A[5] | A[4]
011 | A[6] | A[7]
100 | A[9] | A[8]
101 | A[10] | A[11]
110 | x[3] | x[11]
111 | x[15] | x[7]
addr | BANK0 | BANK1
000 | A[0] | A[1]
001 | A[3] | A[2]
010 | A[5] | A[4]
011 | A[6] | A[7]
100 | A[9] | A[8]
101 | A[10] | A[11]
110 | A[12] | A[13]
111 | x[15] | x[7]

## Slide 79: Vertex Coloring
addr | BANK0 | BANK1
000 | A[0] | A[1]
001 | A[3] | A[2]
010 | A[5] | A[4]
011 | A[6] | A[7]
100 | A[9] | A[8]
101 | A[10] | A[11]
110 | A[12] | A[13]
111 | A[15] | A[14]
addr | BANK0 | BANK1
000 | B[0] | A[1]
001 | A[3] | B[2]
010 | A[5] | A[4]
011 | A[6] | A[7]
100 | A[9] | A[8]
101 | A[10] | A[11]
110 | A[12] | A[13]
111 | A[15] | A[14]
addr | BANK0 | BANK1
000 | B[0] | B[1]
001 | B[3] | B[2]
010 | A[5] | A[4]
011 | A[6] | A[7]
100 | A[9] | A[8]
101 | A[10] | A[11]
110 | A[12] | A[13]
111 | A[15] | A[14]
addr | BANK0 | BANK1
000 | B[0] | B[1]
001 | B[3] | B[2]
010 | A[5] | B[4]
011 | B[6] | A[7]
100 | A[9] | A[8]
101 | A[10] | A[11]
110 | A[12] | A[13]
111 | A[15] | A[14]

## Slide 80: Vertex Coloring
addr | BANK0 | BANK1
000 | B[0] | B[1]
001 | B[3] | B[2]
010 | B[5] | B[4]
011 | B[6] | B[7]
100 | A[9] | A[8]
101 | A[10] | A[11]
110 | A[12] | A[13]
111 | A[15] | A[14]
addr | BANK0 | BANK1
000 | B[0] | B[1]
001 | B[3] | B[2]
010 | B[5] | B[4]
011 | B[6] | B[7]
100 | A[9] | B[8]
101 | B[10] | A[11]
110 | A[12] | A[13]
111 | A[15] | A[14]
addr | BANK0 | BANK1
000 | B[0] | B[1]
001 | B[3] | B[2]
010 | B[5] | B[4]
011 | B[6] | B[7]
100 | B[9] | B[8]
101 | B[10] | B[11]
110 | A[12] | A[13]
111 | A[15] | A[14]
addr | BANK0 | BANK1
000 | B[0] | B[1]
001 | B[3] | B[2]
010 | B[5] | B[4]
011 | B[6] | B[7]
100 | B[9] | B[8]
101 | B[10] | B[11]
110 | B[12] | A[13]
111 | A[15] | B[14]

## Slide 81: Vertex Coloring
addr | BANK0 | BANK1
000 | B[0] | B[1]
001 | B[3] | B[2]
010 | B[5] | B[4]
011 | B[6] | B[7]
100 | B[9] | B[8]
101 | B[10] | B[11]
110 | B[12] | B[13]
111 | B[15] | B[14]
addr | BANK0 | BANK1
000 | C[0] | B[1]
001 | B[3] | B[2]
010 | B[5] | C[4]
011 | B[6] | B[7]
100 | B[9] | B[8]
101 | B[10] | B[11]
110 | B[12] | B[13]
111 | B[15] | B[14]
addr | BANK0 | BANK1
000 | C[0] | C[1]
001 | B[3] | B[2]
010 | C[5] | C[4]
011 | B[6] | B[7]
100 | B[9] | B[8]
101 | B[10] | B[11]
110 | B[12] | B[13]
111 | B[15] | B[14]
addr | BANK0 | BANK1
000 | C[0] | C[1]
001 | B[3] | C[2]
010 | C[5] | C[4]
011 | C[6] | B[7]
100 | B[9] | B[8]
101 | B[10] | B[11]
110 | B[12] | B[13]
111 | B[15] | B[14]

## Slide 82: Vertex Coloring
addr | BANK0 | BANK1
000 | C[0] | C[1]
001 | C[3] | C[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | B[9] | B[8]
101 | B[10] | B[11]
110 | B[12] | B[13]
111 | B[15] | B[14]
addr | BANK0 | BANK1
000 | C[0] | C[1]
001 | C[3] | C[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | B[9] | C[8]
101 | B[10] | B[11]
110 | C[12] | B[13]
111 | B[15] | B[14]
addr | BANK0 | BANK1
000 | C[0] | C[1]
001 | C[3] | C[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | C[9] | C[8]
101 | B[10] | B[11]
110 | C[12] | C[13]
111 | B[15] | B[14]
addr | BANK0 | BANK1
000 | C[0] | C[1]
001 | C[3] | C[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | C[9] | C[8]
101 | C[10] | B[11]
110 | C[12] | C[13]
111 | B[15] | C[14]

## Slide 83: Vertex Coloring
addr | BANK0 | BANK1
000 | C[0] | C[1]
001 | C[3] | C[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | C[9] | C[8]
101 | C[10] | C[11]
110 | C[12] | C[13]
111 | C[15] | C[14]
addr | BANK0 | BANK1
000 | Y[0] | C[1]
001 | C[3] | C[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | C[9] | Y[8]
101 | C[10] | C[11]
110 | C[12] | C[13]
111 | C[15] | C[14]
addr | BANK0 | BANK1
000 | Y[0] | Y[1]
001 | C[3] | C[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | Y[9] | Y[8]
101 | C[10] | C[11]
110 | C[12] | C[13]
111 | C[15] | C[14]
addr | BANK0 | BANK1
000 | Y[0] | Y[1]
001 | C[3] | Y[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | Y[9] | Y[8]
101 | Y[10] | C[11]
110 | C[12] | C[13]
111 | C[15] | C[14]

## Slide 84: Vertex Coloring
addr | BANK0 | BANK1
000 | Y[0] | Y[1]
001 | Y[3] | Y[2]
010 | C[5] | C[4]
011 | C[6] | C[7]
100 | Y[9] | Y[8]
101 | Y[10] | Y[11]
110 | C[12] | C[13]
111 | C[15] | C[14]
addr | BANK0 | BANK1
000 | Y[0] | Y[1]
001 | Y[3] | Y[2]
010 | C[5] | Y[4]
011 | C[6] | C[7]
100 | Y[9] | Y[8]
101 | Y[10] | Y[11]
110 | Y[12] | C[13]
111 | C[15] | C[14]
addr | BANK0 | BANK1
000 | Y[0] | Y[1]
001 | Y[3] | Y[2]
010 | Y[5] | Y[4]
011 | C[6] | C[7]
100 | Y[9] | Y[8]
101 | Y[10] | Y[11]
110 | Y[12] | Y[13]
111 | C[15] | C[14]
addr | BANK0 | BANK1
000 | Y[0] | Y[1]
001 | Y[3] | Y[2]
010 | Y[5] | Y[4]
011 | Y[6] | C[7]
100 | Y[9] | Y[8]
101 | Y[10] | Y[11]
110 | Y[12] | Y[13]
111 | C[15] | Y[14]

## Slide 85
Simple DPBRAM
  Vertex Coloring
    DIF
    DIT
  Block Diagram
  Timing Diagram
  Verilog Implementation
  Simulation Results

## Slide 86: Block Diagram
out_BF1
BANK1
(32x8)
BANK0
(32x8)
MULT.v
BF.v
ROM
(32x8)
REGD
REGE
0 1
1 0
1 0
1 0
sel_wr_bank
sel_din
sel_wr_swap
REGC
REGA
REGB
0 1
1 0
sel_rd_swap
1 0
ext_data_in
data_wr_BANK1
data_wr_BANK0
data_rd_BANK0
data_rd_BANK1
out_BF0
out_REG_A
out_REG_B
out_FFT1
out_FFT0
out_REG_A
out_REG_B
out_MULT
out_REG_C
out_REG_D
out_REG_E
out_dout
out_change1
out_change0
out_bank1
out_bank0
out_swap1
out_swap0
data_rd_ROM
ext_data_out
BANK3
(32x8)
BANK2
(32x8)
data_wr_BANK0
data_wr_BANK1
AGU
WR
AGU
RD
TopFFT
RD
WR
FFT
controller
sel_din 1일경우 ext_data_in, sel_wr_bank로 BANK 선택 후 차례대로 data_wr_BANK 값에 할당.
data_rd_BANK 값 Vertex Coloring 알고리즘에 맞게 Read(AGU에서 address 생성) 이후 sel_swap 신호로 REG_A, REG_B에 저장.
FFT 모듈로 연산 진행 후 STAGE_4일 경우 REG_C로 출력 이외의 경우 REG_D, REG_E에 입력 후 알고리즘에 맞게 sel_swap 신호로
BANK에 저장.
sel_rd_swap
sel_din
sel_wr_swap
1
0
sel_out_bank

## Slide 87: Block Diagram
Address Generator
cnt_addr
cnt_dly
SH1
SH0
Switch
REG_SH1
REG_SH0
cnt
iter, on
addr_BANK1
addr_BANK0
out_REG_SH0
out_REG_SH1
out_sh0
out_sh1
Pre-stage와 Data out address 생성을 위해서 RD, WR인지에 따라 cnt에 cnt_wr 또는 cnt_rd 연결
iter와 on신호에 따라 작동되는 cnt_addr과 1 cycle delay counter cnt_dly를 입력으로 하여 SH로 임시 address 생성, 이후 Switch 로직을 이용해
Vertex Coloring에 맞는 address 생성 후 출력
AGU

## Slide 88: Block Diagram
Bit-reverse Unit
  DIF has bit-reversed output, so it must be converted.

## Slide 89
Simple DPBRAM
  Vertex Coloring
    DIF
    DIT
  Block Diagram
  Timing Diagram
  Verilog Implementation
  Simulation Results

## Slide 90: Block Diagram
DIF-DIT consecutive Implementation
  DIF has natural order inputs and bit-reversed outputs.
  Output address of DIF is mapped to bit-reversed DIT inputs
  Don’t need extra stage for data input or bit-reversing
IN
1
2
3
4
OUT
IN
1
2
3
4
OUT
IN
1
2
3
4
OUT
IN
1
2
3
4
OUT

## Slide 91: Timing Diagram
Simple DPRAM DIF 16pt

## Slide 92: Timing Diagram
Simple DPRAM DIF 16pt
AGU
AGU
READ 1 cycle
REG 1 cycle
REG 1 cycle
DATA OUT
DATA IN
DATA IN
31 cycles for computation
15 cycles for data in
15 cycles for data out

## Slide 93
Simple DPBRAM
  Vertex Coloring
    DIF
    DIT
  Block Diagram
  Timing Diagram
  Verilog Implementation
  Simulation Results

## Slide 94: RD, WR
RD, WR

## Slide 95: AGU
iter, on

## Slide 96: AGU
out_sh
addr_BANK

## Slide 97: Controller
FSM

## Slide 98: Controller
Control signals

## Slide 99: Controller
Counters

## Slide 100
Simple DPBRAM
  Vertex Coloring
    DIF
    DIT
  Block Diagram
  Timing Diagram
  Verilog Implementation
  Simulation Results

## Slide 101: Pre-stage
RUN

## Slide 102: Stage 1 ~ 2

## Slide 103: Stage 3 ~ 4

## Slide 104: Data out

## Slide 105: Simulation Result
Simple DPBRAM 16pt
  Behavioral simulation
  Post-Synthesis Timing simulation
  Post-Implementation Timing simulation

## Slide 106: Simulation Result
Simple DPBRAM 16pt

## Slide 107: True DPBRAM

## Slide 108: True DPBRAM
True DPBRAM
  Block Diagram
  Timing Diagram
  Verilog Implementation
  Simulation Results

## Slide 109: Block Diagram
AMEM
(32x16)
BMEM
(32x16)
MULT
REG_B
REG_A
BF
mux
mux
CROM
(32x8)
controller
OMEM
(32x16)
input
input
FFTcore
TopFFT
FFT
out_mux0
out_mux1
out_MULT
out_REG_A
out_REG_B
out_BF0
out_BF1
ext_data_output0
ext_data_output1
ext_data_input0
ext_data_input1
out_FFTcore0
out_FFTcore1
out_FFTcore0
out_FFTcore1
out_FFT1
out_FFT0
out_FFTcore0
out_FFTcore1
sel_input
sel_input
sel_mux
sel_mux

## Slide 110: Block Diagram
Reuse the modules BF and MULT
AMEM and BMEM have two ports
  Different address for each port
Almost same with SPBRAM architecture but slight changes due to the double-port memory.
  No REG_C for storing BF result; Pipeline depth = 2
  Elements for BF computation can be accessed simultaneously from AMEM or BMEM

## Slide 111: True DPBRAM
True DPBRAM DIT 16pt

## Slide 112: True DPBRAM
True DPBRAM DIT 16pt
36 cycles for comuptation
7 cycles for data in
7 cycles for data out
DATA IN
DATA IN
AMEM >> BMEM
AMEM >> BMEM
BMEM >> AMEM
BMEM >> OMEM
DATA OUT

## Slide 113: Radix-2 16pt DIT MBFFT
Two address for each memory
  addr0 and addr1
Only one register enable
  Parallel data access
  Pipeline depth = 2
(N+1) bits for counters
N bits for state parameters

## Slide 114: Radix-2 16pt DIT MBFFT
Only cstate_out is changed due to pipeline depth
  cnt_out == LCNT – 2 >> cnt_out == LCNT – 1
All counters are same with SPBRAM architecture

## Slide 115: Radix-2 16pt DIT MBFFT
Control signals
Slight change due to pipeline depth is reduced to 2
Only one en_REG due to parallel data access
  ~en_REG; Every stage but IDLE after 2 cycles

## Slide 116: Radix-2 16pt DIT MBFFT
Address
Same as SPBRAM case but it doesn’t need to be accessed sequentially.
Parallel access reduce the computation cycle for every stage.
From SPBRAM address (i,j)
  Stage1 (0,1), (2,3), (4,5), (6,7), (8,9), (10,11), (12,13), (14,15)
  Stage2 (0,2), (1,3), (4,6), (5,7), (8,10), (9,11), (12,14), (13,15)
  Stage3 (0,4), (1,5), (2,6), (3,7), (8,12), (9,13), (10,14), (11,15)
  Stage4 (0,8), (1,9), (2,10), (3,11), (4,12), (5,13), (6,14), (7,15)
  addr0 = i, addr1 = j

## Slide 117: Radix-2 16pt DIT MBFFT
AMEM(32x16) |  |  |  |  |  |  |  |  |  |  |  |  | 
cstate |  | IDLE |  | STAGE_1 |  | STAGE_2 |  | STAGE_3 |  | STAGE_4 |  | STAGE_1 | 
addr0 | addr1 | data0 | data1 | data0 | data1 | data0 | data1 | data0 | data1 | data0 | data1 | data0 | data1
0000 | 0000 | x[0] | x[8] | x[0] | x[8] | b[0] | b[2] | b[0] | b[2] | x2[0] | x2[1] | x2[0] | x2[1]
0001 | 0001 | x[4] | x[12] | x[4] | x[12] | b[1] | b[3] | b[1] | b[3] | x2[4] | x2[3] | x2[4] | x2[3]
0010 | 0010 | x[2] | x[10] | x[2] | x[10] | b[4] | b[6] | b[4] | b[6] | x2[2] | x2[5] | x2[2] | x2[5]
0011 | 0011 | x[6] | x[14] | x[6] | x[14] | b[5] | b[7] | b[5] | b[7] | x2[6] | x2[7] | x2[6] | x2[7]
0100 | 0100 | x[1] | x[9] | x[1] | x[9] | b[8] | b[10] | b[8] | b[10] | x2[8] | x2[9] | x2[8] | x2[9]
0101 | 0101 | x[5] | x[5] | x[5] | x[5] | b[9] | b[11] | b[9] | b[11] | x2[10] | x2[11] | x2[10] | x2[11]
0110 | 0110 | x[3] | x[11] | x[3] | x[11] | b[12] | b[14] | b[12] | b[14] | x2[12] | x2[13] | x2[12] | x2[13]
0111 | 0111 | x[7] | x[15] | x[7] | x[15] | b[13] | b[15] | b[13] | b[15] | x2[14] | x2[15] | x2[14] | x2[15]
BMEM(32x16) |  |  |  |  |  |  |  |  |  |  |  |  | 
cstate |  | IDLE |  | STAGE_1 |  | STAGE_2 |  | STAGE_3 |  | STAGE_4 |  | STAGE_1 | 
addr0 | addr1 | data0 | data1 | data0 | data1 | data0 | data1 | data0 | data1 | data0 | data1 | data0 | data1
0000 | 0000 |  |  | a[0] | a[1] | a[0] | a[1] | c[0] | c[4] | c[0] | c[4] | a2[0] | a2[1]
0001 | 0001 |  |  | a[2] | a[3] | a[2] | a[3] | c[1] | c[5] | c[1] | c[5] | a2[2] | a2[3]
0010 | 0010 |  |  | a[4] | a[5] | a[4] | a[5] | c[2] | c[6] | c[2] | c[6] | a2[4] | a2[5]
0011 | 0011 |  |  | a[6] | a[7] | a[6] | a[7] | c[3] | c[7] | c[3] | c[7] | a2[6] | a2[7]
0100 | 0100 |  |  | a[8] | a[9] | a[8] | a[9] | c[8] | c[12] | c[8] | c[12] | a2[8] | a2[9]
0101 | 0101 |  |  | a[10] | a[11] | a[10] | a[11] | c[9] | c[13] | c[9] | c[13] | a2[10] | a2[11]
0110 | 0110 |  |  | a[12] | a[13] | a[12] | a[13] | c[10] | c[14] | c[10] | c[14] | a2[12] | a2[13]
0111 | 0111 |  |  | a[14] | a[15] | a[14] | a[15] | c[11] | c[15] | c[11] | c[15] | a2[14] | a2[15]
OMEM(32x16) |  |  |  |  | 
cstate |  | STAGE_4 |  | STAGE_1 | 
addr0 | addr1 | data0 | data1 | data0 | data1
0000 | 0000 | y[0] | y[8] | y[0] | y[8]
0001 | 0001 | y[1] | y[9] | y[1] | y[9]
0010 | 0010 | y[2] | y[10] | y[2] | y[10]
0011 | 0011 | y[3] | y[11] | y[3] | y[11]
0100 | 0100 | y[4] | y[12] | y[4] | y[12]
0101 | 0101 | y[5] | y[13] | y[5] | y[13]
0110 | 0110 | y[6] | y[14] | y[6] | y[14]
0111 | 0111 | y[7] | y[15] | y[7] | y[15]
CROM(32x8) | 
Addr | Data
0000 | 00007FFE
0001 | CF047642
0010 | A57E5A82
0011 | 89BE30FC
0100 | 80020000
0101 | 89BECF04
0110 | A57EA57E
0111 | CF0489BE

## Slide 118: Radix-2 16pt DIT MBFFT
AMEM Address

## Slide 119: Radix-2 16pt DIT MBFFT
BMEM Address

## Slide 120: Radix-2 16pt DIT MBFFT
OMEM, CROM Address

## Slide 121: Radix-2 16pt DIT MBFFT
Testbench
  Two values are coming out simultaneously
  RTLout.txt
  01 ext_data_output0[31:16]
  02 ext_data_output0[15:0]
  03 ext_data_output1[31:16]
  04 ext_data_output1[15:0]
  05 ext_data_output0[31:16]
  06 ext_data_output0[15:0]
  07 ext_data_output1[31:16]
  08 ext_data_output1[15:0]
  ∙
  ∙
  ∙
  8191 ext_data_output1[31:16]
  8192 ext_data_output1[15:0]

## Slide 122: Pre-stage
ext_data_in
in_vld
RUN
PRE_IN

## Slide 123: Stage 1
STAGE_1
AMEM
data_rd_AMEM
STAGE_1 O/P
data_rd_BMEM
1 cycle
1 cycle

## Slide 124: Stage 2

## Slide 125: Stage 3

## Slide 126: Stage 4

## Slide 127: Set 2

## Slide 128: Simulation Result
True DPBRAM 16pt
  Behavioral simulation
  Post-Synthesis Timing simulation
  Post-Implementation Timing simulation

## Slide 129: Simulation Result
DPBRAM 16pt

## Slide 130: Reference
[1] Hsin-Fu Lo, Ming-Der Shieh and Chien-Ming Wu, "Design of an efficient FFT processor for DAB system," ISCAS 2001. The 2001 IEEE International Symposium on Circuits and Systems (Cat. No.01CH37196), Sydney, NSW, Australia, 2001, pp. 654-657 vol. 4, doi: 10.1109/ISCAS.2001.922322.